Titel
Tutorial GiBUU
Part B: Hands-On (HiLepton init)
      GiBUU implementation
      Hands On: Final state with HiLepton init

---
Testparticle ansatz
BUU: Testparticle ansatz
- idea:
  approximate full phase-space density distribution by a
  sum of delta-functions
- each delta-function represents one (test-)particle
  with a sharp position and momentum
- large number of test particles needed
f(\vec r,t,\vec p\,)\sim\sum_{i=1}^{N_{\rm test}} \delta\left(\vec r-\vec r_i(t)\right) \delta\left(\vec p-\vec p_i(t)\right)
\left[\partial_t+(\nabla_pH_i)\nabla_r-(\nabla_rH_i)\nabla_p\right]f_i(\vec r,t,\vec p\,)=C\left[f_i,f_j,\dots\right]

---
Nuclear ground state
Nuclear ground state
- density distribution: Woods-Saxon (or harm. Oscillator)
- particle momenta: ‘Local Thomas-Fermi approximation’
- Fermi-momentum:
- Fermi-energy:
“GiBUU is semiclassical”
no nuclear excitations
energy/momentum transfer > 50 MeV
p_{F{\rm (n,p)}}(\vec r\,)=\left(3\pi^2\rho_{\rm (n,p)}(\vec r\,)\right)^{1/3}
E_{F{\rm (n,p)}}=\sqrt{p_{F{\rm (n,p)}}^2+m_N^2} +U_{\rm (n,p)}(\vec r,p_F)
f_{\rm (n,p)}(\vec r,\vec p\,)=\Theta\left[p_{F{\rm(n,p)}}(\vec r\,)-|\vec p\,|\right]

---
Nuclear ground state
- improvement: ensure constant Fermi-Energy
- needs iteration for mom.dep potential
- important for QE-peak	(Gallmeister, Mosel, Weil, PRC94 (2016) 035502)
non-mom.dep potential, asymmetry-term, Coulomb

---
Init
Init
in principle:
  1. initialize nucleons
  2. perform one initial elementary event on one nucleon
  3. propagate nucleons and final state particles
- correct, but ‘waste of time’
- idea:
  final state particles do not really disturb the nucleus
- 2 particle classes:
  - ‘real particles’
  - ‘perturbative particles’

---
particle classes
Particle classes
- ‘real particles’
  - nucleons
  - may interact among each other
  - interaction products are again ‘real particles’
- ‘perturbative particles’
  - final state particles of initial event
  - may only interact with ‘real particles’
  - interaction products are again ‘perturbative particles’
- ‘real particles’ behave as if other particles are not there
- total energy, total baryon number, etc. not conserved!

---
perturbative init
Init with perturbative particles
init
  1. initialize nucleons
  2. perform one initial elementary event on every nucleon
  3. propagate nucleons and final state particles
  - final states particles are ‘perturbative particles’
  - different final states do not interfere
- every final state particle gets a ‘perturbative weight’:
  - value: cross section of initial event
  - is inherited in every FSI
  - for final spectra the ‘perturbative weights’ have to be added, not only the particle numbers

---
perturbative init 2
Init with perturbative particles
- idea:
  simple workaround against oscillating ground states:
  freeze nucleon testparticles
- since nucleons are real particles, their interactions among each other should not influence final state particles
- advantage: computational time
- disadvantage: ???

---
Website
The GiBUU website
https://gibuu.hepforge.org
- central place for all information on GiBUU
- based on a wiki system (‘trac’)
- contains lots of information about the model and code
- documentation of input parameters, output files etc.
- source code viewer for svn repository
- timeline of news & changes
- cross section plotter (for hadronic interactions)

---
Cross section Plotter
Cross section plotter
https://gibuu.hepforge.org/XSection/

---
Prerequisites
Technical Prerequisites
- GiBUU runs on Linux, Mac, Windows
- Linux is preferred platform
- needed software tools:
  - subversion (for code checkout)
  - GNU make
  - a Fortran compiler (e.g. gfortran 5.4)
  - perl
  - libbz2
  - (a running ROOT installation)
  - see website for supported compilers
  - private observation: ifort generates fastest code
for output in ROOT format
        via RootTuple library:
 https://roottuple.hepforge.org/

---
Getting the code svn
Getting the code
- ...via check-out from svn repository
- create a new directory
  mkdir GiBUU; cd GiBUU
- check-out the code
  svn co http://gibuu.hepforge.org/svn/releases/release2017
- check out the input files
  svn co http://gibuu.hepforge.org/svn/releases/buuinput2017 ./buuinput
git access (GitHub) possible, but not really maintained
HEPFORGE UPGRADE 2018

---
Getting the code tar
Getting the code
/trac/wiki/download
- ...via tar-balls
- create a new directory
  mkdir GiBUU; cd GiBUU
- download the code
  wget –content-disposition →
  →https://gibuu.hepforge.org/downloads?f=release2019.tar.gz
  tar -xzvf release2019.tar.gz
- download the input files
  wget –content-disposition →
  →https://gibuu.hepforge.org/downloads?f=buuinput2019.tar.gz
  tar -xzvf buuinput2019.tar.gz
- (download RootTuple library)
  wget –content-disposition →
  →https://gibuu.hepforge.org/downloads?f=libraries2019_RootTuple.tar.gz
  tar -xzvf libraries2019_RootTuple.tar.gz

---
Getting the code
- ...via docker
- initiative by Luke Pickering:
  https://hub.docker.com/r/picker24/gibuu_2019
- … is this a way to go?
  (feedback/input very welcome!!!)

---
Compiling the code
Compiling the code
/trac/wiki/compiling
- go to directory and make!
  cd release2019; make
  (cd release2019; make buildRootTuple; make withROOT=1)
- takes about 3 minutes on my laptop (one core)
- parallel make
  make -j 4
- choosing a compiler
  make FORT=gfortran-4.8
- no optimization
  make MODE=opt0
- re-compile everything
  make renew
if something went wrong...
SUCCESS: GiBUU.x generated.

---
Updating the code
Updating the code via svn
- from time to time there will be changes in the code
  (bugfixes, new features, …)
- latest release: GiBUU 2017 (Oct. 29, 2017)
- you should keep your local copy of the code up to date
- do in the code directory:
  svn update
- check output for modified files and conflicts
- after updating, you need to recompile
  make
HEPFORGE UPGRADE 2018

---
Running the code
Running the code
- after successful compilation, there is the executable
   ./objects/GiBUU.x (linked also ./testRun/GiBUU.x)
- run the executable with input and output files
  ./GiBUU.x < input.job > log.txt
- either
  - run ‘in-tree’, i.e. in the directory testRun
    cd testRun; ./GiBUU.x
  - copy it somewhere else
  - use it from somewhere else with full path
- the file ‘log.txt’ will contain a log of GiBUU control & debug messages, physics output will be written to other files
recommended,
since several output files are generated

---
Input parameters 1
Input parameters
- input via the Fortran way: ‘jobcard’
          (= plain text file with data in some specific format)
          sample jobcards in ./testRun/jobCards
- format: data in a ‘jobcard’ is grouped in ‘namelists’
- capitalization (upper/lower case) does not matter
\begin{verbatim} &namelist1 switch1 = value1 ! some comment switch2 = value2 ! another comment / &namelist2 switch3 = value3 switch4 = value4 / \end{verbatim}

---
Input parameters 2
Input parameters
- there are a lot of input parameters!
- documented at website
  https://gibuu.hepforge.org/Documentation2019/code/robo_namelist.html	https://gibuu.hepforge.org/Documentation2019/namelists.pdf
- most of them not relevant for beginners
- most of them have reasonable default values
- some relevant namelists for neutrino events:
  - ‘input’ (basics)
  - ‘HiLeptonNucleus’
  - ‘target’
  - ‘EventOutput’ (producing particle output)
  - ...

---
Namelist 'input'
The Namelist ‘input’
014_HiLepton_A.job
- the basic settings that need to be supplied
- ‘path_to_input’ must point to local path of buuinput directory
&input
      eventtype = 14 ! HiLepton
      numEnsembles = 1000
      numTimeSteps = 200
      delta_T = 0.1 ! time step size
      length_perturbative = 2000 ! okay up to ..., Xe
      num_runs_SameEnergy=1 ! number of runs per energy
      localEnsemble = .TRUE.
      freezeRealParticles = .TRUE.
      path_To_Input = '~/GiBUU/buuinput'
/

---
Namelist neutrino_induced
The Namelist ‘HiLeptonNucleus’
014_HiLepton_A.job
infos about the elementary electron event
&HiLeptonNucleus
! shadow = F
! DoStatistics = T ! additional output
      iExperiment= 5 ! JLAB, 5GeV
      iDetector = -1 ! use default
/

---
The Namelist ‘HiLeptonNucleus’
iExperiment:
    0: no experiment/fixed kinematics
    1: Hermes, 27GeV, D,N,Kr
    2: Hermes, 27GeV, Ne
    3: Hermes, 27GeV, H
    4: JLAB, 12GeV
    5: JLAB, 5GeV
    6: EMC, 100GeV
    7: EMC, 120GeV
    8: EMC, 200GeV
    9: EMC, 280GeV
  10: Hermes, 12GeV
  11: Hermes, 27GeV, arXiv:0704.3270
  12: Mainz, Yoon: Ebeam=1.5GeV
  13: Hermes, 27GeV, arXiv:0704.3712 (pT-broadening)
  14: JLAB, 5GeV, rho0 experiment
  15: JLAB, 4GeV, rho0 experiment
  16: EIC, E_e and E_A given explicit (3+30,11+30,4+100)
  17: no detector, total cross section, Ebeam
  18: E665, 470GeV
  19: CLAS/JLAB, 12GeV RunGroupA optimized 10.6 GeV
  20: CLAS/JLAB, 12GeV RunGroupA theoterical
defines the electron kinematics:
acceptance cuts
efficiency
hadronic cuts for online analysis

---
The Namelist ‘HiLeptonNucleus’
- iDetector:
- additional cuts:
 -1 : use default
  0 : no detector
  1 : HERMES, full efficiency
  2 : EMC, full efficiency
  3 : CLAS, only cuts (th_e=12°..50°, th_hadron=6°..143°)
  4 : CLAS, full efficiency + cuts as for 5GeV
  5 : CLAS, electron: cuts (th_e=12°..50°),
        hadrons: efficiency+cuts as for 5GeV
90 : full acceptance
&HiLeptonNucleus
...
! user_numin = ... ! GeV
! user_numax = ... ! GeV
! user_costmin = ...
! user_costmax = ...
! user_smin = ... ! GeV^2
! user_qsqmin = ... ! GeV^2
! user_qsqmax = ... ! GeV^2
...
/

---
Fixed electron kinematics
fix kinematics by electronic variables:
&HiLeptonNucleus
...
      iExperiment=17 ! no detector, total cross section, Ebeam
! iDetector = 0
      Ebeam = ... ! GeV
...
/
calculates total cross section
(cuts by user_… as above)

---
Fixed photon kinematics
fix the kinematics by photonic variables:
&HiLeptonNucleus
...
      iExperiment= 0 ! no experiment/fixed kinematics
! iDetector = 0
...
/
&HiPhotonKinematics
    nu = ...
    Q2 = ...
    eps = ...
    srts = ...
    W = ...
    xBj = ...
    Ebeam = ...
/
exactly 3 of them
have to be given

---
EIC kinematics
will be boosted to fixed target kinematics
&HiLeptonNucleus
...
      iExperiment=16 ! EIC
! iDetector = 0
      EIC_Ee=3 ! GeV, energy electron
      EIC_EA=30 ! GeV, energy nucleus
...
/

---
Namelist Target
The Namelist ‘target’ etc.
014_HiLepton_A.job
- infos about the nucleus as target
- analytic density treatment
\begin{lstlisting}[basicstyle=\ttfamily] &target Target_A = 12 Target_Z = 6 ! ReAdjustForConstBinding = T / \end{lstlisting}
\begin{lstlisting}[basicstyle=\ttfamily] &initDensity densitySwitch = 2 ! 2=analytic / &initPauli pauliSwitch = 2 ! 2=analytic / \end{lstlisting}

---
Potentials
014_HiLepton_A.job
for high energies:
&baryonPotential
      noPerturbativePotential = T ! perturbative baryons feel no potential
/
&mesonPotential
      noPerturbativePotential = T ! perturbative mesons feel no potential
/

---
Analysis strategies
Analysis strategies
- ‘on-line’ analysis directly inside GiBUU
  - direct analysis of desired quantity during the simulation
  - directly produce histograms etc.
  - no intermediate particle output
  - advantage: access to all internal information
  - disadvantage: needs recompilation for changes
  - mainly only for developers
- ‘off-line’ analysis
  - output all particles/events
  - LesHouches/ROOT format, proprietary format
  - analysis may be changed after simulation run
  - disadvantage: may produce large amount of data
- GiBUU tends to be ‘silent’ by default

---
On-Line
1) on-line analysis
- mainly useful for developers
- see code/analysis/HiLeptonAnalysis.f90 for details
&HiLepton_Analysis
! DoLeptonKinematics = T
! DoHadronKinematics = T
! DoTimes = T
! DoOutChannels = T
! DoInvMasses = T
! DoFindRho0 = T
! DoClasie = T
! DoMorrow = T
! DoClassifyFirst = T
/

---
Namelist EventOutput
2) off-line analysis: The Namelist ‘EventOutput’
014_HiLepton_A.job
- generate particle output
- output only for perturbative particles
- file(s) generated ‘EventOutput.Pert.*.lhe’
- possible formats:
  1. LesHouches	http://arxiv.org/abs/hep-ph/0609017
  2. OSCAR 2013	http://phy.duke.edu/~jeb65/oscar2013
  3. Shanghai 2014	http://www.physics.sjtu.edu.cn/hic2014/node/12
  4. ROOT
\begin{lstlisting}[basicstyle=\ttfamily] &EventOutput WritePerturbativeParticles = T WriteRealParticles = F ! EventFormat = 1 ! 1=LesHouches / \end{lstlisting}

---
Les Houches format
Output format ‘Les Houches’
- XML-like event format
- named after a town in France
- basic structure:
arXiv:hep-ph/0609017v1
\begin{lstlisting}[basicstyle=\ttfamily,language=XML] <LesHouchesEvents version="1.0"> <header> ... </header> <init> ... </init> <event> ... </event> ... (any number of <event> blocks can follow) ... \end{lstlisting}

---
Les Houches format event
Output format ‘Les Houches’ (2)
<event>
     3 0 1.222E+1 0.000E+0 0.000E+0 0.000E+0
    2112 0 0 0 0 0 1.827E-1 -1.468E-1 2.975E+0 3.128E+0 9.380E-1 0. 9.
    -211 0 0 0 0 0 -1.045E-1 1.092E-2 1.015E+0 1.030E+0 1.380E-1 0. 9.
    -211 0 0 0 0 0 4.420E-2 8.971E-2 3.135E-2 1.732E-1 1.380E-1 0. 9.
# 14 3.520E+0 1.808E+0 4.946E-1 1.708E+0 2004
</event>
- line 1: N=number of lines, 0, weight, boring zeros
- following: N lines, representing one particle each
  columns: 1 = ID (PDG code), 7-9 = px,y,z, 10 = E, 11 = mass
- last line: comment
  ‘magic number’ 14 = special info for HiLepton events
  nu, Q2, eps, phiLepton, eventtype
- eventtype: 2001 = Pythia VMD, …, 2004 = Pythia DIS, …

---
Analysis using ‘Les Houches’
#!/usr/bin/env python3
from pylhef import *
data = read("EventOutput.Pert.00000001.lhe")
sigmatot = 0
sigmapi = 0
for ev in data.events:
    sigmatot += ev.weight
    for part in ev.particles:
        if (part.id==211):
        sigmapi += ev.weight
print("sigmatot = ",sigmatot)
print("sigmapi = ",sigmapi)
https://github.com/jrvidal/pylhef
sum up the weights!
sigmatot = 30628.30051
sigmapi = 21461.13987
\sigma(e^- A)/A = 15.314\,\mu{\rm b}
\sigma(e^- A\to\pi^+X)/A = 10.731\,\mu{\rm b}
\frac{1}{n_{\rm Ens}\cdot A}

---
Output format ‘ROOT’
- same info as in LesHouches files
- needs:
  - working ROOT installation
  - building RootTuple library (included in GiBUU)
  - linking GiBUU with RootTuple
  - setting ‘EventFormat = 4’ in Jobcard
- … (I have no experience with ROOT; input/feedback welcome!!!)
- work in progress:
          patch to additionally write positional info

---
‘Tuning’
- modify cross sections of different channels/eventtypes:
  multiply perweights with a factor
- implement own processes/particles:
  difficult
- … ?
- Event output
  please contact me!!!

---
Homework
Homework
- Exercise:
  - Develop a jobcard, which describes your beloved experiment.
  - Run GiBUU with this input.
  - Develop some analysis scripts, which creates the desired plots.
    (You have to read particle/event output in LesHouches format.)

---
BUU@Gießen
BUU@Gießen and GiBUU
- long history
  1986: first code	(W.Bauer)
  ~1996: rewrite of code	(S.Teis, M.Effenberger)
  ~2005: rewrite of code	(O.Buss)
- actual version: „GiBUU“
  - modular, Fortran 2003, single threaded
  - semi-automatic documentation (robodoc)
  - version control (svn + trac)
- bottlenecks:
  - PYTHIA	(very slow at low energies)
  - huge code	(185 000 lines + docu + 'externals')
  - „long history“	(old structures)
  - …
  - transparency ratios = ratios of MC calculations: ~50 weeks per curve
lifetime: ~10 yrs

---
People
People
- Oliver Buss
- Theo Gaitanos, Thessaloniki
- Kai Gallmeister, Frankfurt
- Hendrik van Hees, Frankfurt
- Olga Lalakulich
- Alexei Larionov, Frankfurt
- Tina Leitner
- Ulrich Mosel, Gießen
- Janus Weil
- ~30 registered users

---
Outline
Outline
- Part A: Kinetic Theory and GiBUU implementation
  - ...
- Part B: Hands On
  - GiBUU code
  - details for neutrino event generation